## Slide 1: AdaSense: Adapting Sampling Rates for Activity Recognition in Body Sensor Networks
Xin Qi, Matthew Keally, Gang Zhou, Yantao Li, Zhen Ren
College of William and Mary

## Slide 2: Background - Activity Recognition
Activity Recognition aims to automatically recognize user actions from the patterns (or information) observed on user actions with the aid of computational devices.
Fall Detection
Sleeping Assessment
Depression Detection

## Slide 3: Sensing-based Activity Recognition
Problem setting
Accelerometer
Gyroscope
Temperature
Light
etc.
Sensing Data
Running, Walking, Sitting, …

## Slide 4: A Dilemma
High sensors sampling rate for high recognition accuracy,
Reducing sensors sampling rate to save energy
de-sampled data
accuracy
highly sampled data
accuracy
energy overhead
energy overhead

## Slide 5: Research Question
  How to reduce sensors sampling rate without sacrificing recognition accuracy?
accuracy
energy overhead
How to achieve
?

## Slide 6: Preliminary Experiment
Opportunity data set, 3 subjects, 4 locomotion activities, sensors sampling rate - 30 Hz
Select 8 on-body sensors (4 accel. & gyro.)
Extract features at 30 Hz and select the best ones
At each sampling rate
  Extract the selected features
  Obtain accuracy following 10-cross validation
Classifier – Support Vector Machine (SVM) + Radial-base Function (RBF)
Sequential Forward Strategy (SFS) based Feature Selection Algorithm

## Slide 7: Two Motivating Observations
Blue Line – Activity Detection (Binary Classification)
Red Line – Multi-Activity Classification
Given the feature set,
at each sampling rate,
detection accuracy
≥
multi-class. accuracy
Lemma:
Given the feature set,
for any accuracy
requirement,
minimal necessary rate
for detection
≤
that for multi-class.
=
Implicit fact – diff. feature sets have diff.
minimal necessary sampling rates
Sitting
Lying Down
Standing
Walking

## Slide 8: Outline
How to reduce sensors sampling rate through exploiting the Lemma?
How to reduce sensors sampling rate through exploring feature set space?
Evaluation, related work & conclusion

## Slide 9: AdaSense Architecture
We design Efficient Activity Recognition (EAR) to exploit the Lemma
Exploit the Lemma

## Slide 10: Exploit The Lemma
1. At beginning, EAR identifies current activity with multi-class.
2. EAR informs sampling controller
the predicted activity
3. Sampling controller controls sensors sampling
at the detection sampling rate of the activity
4.With de-sampled data, EAR performs single activity detection
To reduce false report, activity change is detected when
EAR gets four negative activity detection results out of the
most recent five ones.
5. Go back to 1 when an activity change is detected.

## Slide 11: AdaSense in Runtime
Sensors sampling rate is reduced in average!

## Slide 12: AdaSense Architecture
To further reduce sensors sampling rate, AdaSense utilizes Genetic Programming (GP) to explore feature set space
Exploit the Lemma
Explore Feature Set Space

## Slide 13: Exploring Feature Set Space
Genetic Programming
  Optimization objective – minimizing the minimal necessary sampling rate for multi-activity classification under an accuracy requirement
  Minimizing necessary sampling rate for activity detection through minimizing its upper bound (a heuristic method)

## Slide 14: A Variant GP-based Algorithm

## Slide 15: Evaluation - Setup
SVM plus RBF kernel as classifier
SFS based feature selection algorithm
Follow 10-fold cross validation routine to obtain accuracy
GP-based algorithm is implemented upon GPLAB
Set individual height as 3 and population size as 100
Two datasets: Opportunity dataset and a smartphone dataset we collect

## Slide 16: Evaluation - Results for Opportunity Dataset
GP-based algorithm convergence rate
Optimal features for subject one
60 generations are enough for the algo. to converge
Simple structure and operation, low cost.
Xis are the best features in the initial generation

## Slide 17: Evaluation - Results for Opportunity Dataset
Sampling rate reduction for multi-classification
Sampling rate reduction for
activity detection (subject 1)
Chart: 
| Subject 1 | Subject 2 | Subject 3
BFS | 24 | 30 | 25
OFS | 3 | 12 | 9
Sampling Rate (Hz)
BFS – best feature set from initial generation
OFS – optimal feature set
Chart: 
| sitting | lying down | walking | standing
BFS | 5 | 1 | 9 | 3
OFS | 2 | 1 | 3 | 3
Sampling Rate (Hz)

## Slide 18: Evaluation – Collecting Data with Smartphone
8 subjects, 6 activities (sitting, walking, running, lying down, standing, cycling)
Smartphone (Google Nexus One) is put into each subject’s pocket
Each subject performs each activity for 30 minutes
Record the tri-axial accelerometer readings

## Slide 19: Evaluation – Results for Smartphone Dataset
Sampling rate reduction for multi-classification
Chart: 
| S1 | S2 | S3 | S4 | S5 | S6 | S7 | S8
BFS | 18 | 15 | 19 | 15 | 22 | 20 | 17 | 19
OFS | 9 | 10 | 12 | 8 | 11 | 10 | 9 | 7
Sampling Rate (Hz)
BFS – best feature set from initial generation
OFS – optimal feature set

## Slide 20: Evaluation – Results for Smartphone Dataset
Sampling rate reduction for activity detection
Chart: 
| lying down | sitting | standing | running | walking | cycling
BFS | 4 | 6 | 10 | 7 | 8 | 6
OFS | 2 | 3 | 5 | 4 | 4 | 3
Sampling Rate (Hz)
Results of Subject 1
BFS – best feature set from initial generation
OFS – optimal feature set

## Slide 21: Evaluation – Results for Smartphone Dataset
Power measurement result of sensor sampling
Feature extraction and classification,
  Power 3.5mw
  Duration 12.7ms

## Slide 22: Evaluation – Results for Smartphone Dataset
Compared to A3R, a most recent sampling rate reduction method
Energy emulation - multiplies each system state duration by the corresponding energy power consumption per unit time
Energy savings: 39.4%~51.0%

## Slide 23: Related Work
Context-aware sampling rate adaption
  SpeakerSense [Pervasive ‘11], SociableSense [Mobicom ‘11], EmotionSense [Ubicomp ‘10], AR3 [ISWC ‘12]
  Our work achieves more fine-grained sampling rate reduction
Energy saving through sensor cluster selection and duty cycling
  Wolfpack [Infocom ‘11], QoINF [Percom ‘11], Seemon [Mobisys ‘08]
  Our work focuses on sampling rate reduction to save sensing energy

## Slide 24: Limitations
Energy savings achieved by AdaSense are limited for short-term activities
Optimal features may be overfitted to training data.
  We utilize the cross validation method in GP to alleviate overfitting

## Slide 25: Conclusion
AdaSense, a framework to reduce sensors sampling rate for BSN activity recognition.
To achieve that, AdaSense
  Exploits the Lemma: combines multi-activity classification with single activity detection
  Searches an optimal feature set that requires low sampling rate with the aid of GP
AdaSense achieves 39.4%~51.0% sensing energy saving on smartphones compared to a most recent sampling rate reduction method

## Slide 26: Q & A
Thanks!

## Slide 27: Thank You!
The End.

## Slide 28: Explanation for the Lemma
Given a feature set, for single activity a, detection accuracy is
For multi-activity classification, accuracy is
TP – True Positive
TN – True Negative
FN – False Negative
FP – False Positive
A – Activity Set
M – # of classified instances
+
=
= M
≥
1
2

## Slide 29: A Variant GP-based Algorithm
crossover
This picture is excerpted from slides
made by Kumara Sastry, UIUC.
mutation